## Slide 1: COMP 590-154: Computer Architecture
Prefetching

## Slide 2: Prefetching (1/3)
Fetch block ahead of demand
Target compulsory, capacity, (& coherence) misses
  Why not conflict?
Big challenges:
  Knowing “what” to fetch
    Fetching useless blocks wastes resources
  Knowing “when” to fetch
    Too early  clutters storage (or gets thrown out before use)
    Fetching too late  defeats purpose of “pre”-fetching

## Slide 3: Prefetching (2/3)
Without prefetching:
With prefetching:
Or:
Prefetch
Prefetch
Load
L1
L2
Data
DRAM
Total Load-to-Use Latency
Data
Load
Much improved Load-to-Use Latency
Somewhat improved Latency
Data
Load
  Prefetching must be accurate and timely
time

## Slide 4: Prefetching (3/3)
Without prefetching:
With prefetching:
Run
Load
time
  Prefetching removes loads from critical path

## Slide 5: Common “Types” of Prefetching
Software
Next-Line, Adjacent-Line
Next-N-Line
Stream Buffers
Stride
“Localized” (e.g., PC-based)
Pointer
Correlation

## Slide 6: Software Prefetching (1/4)
Compiler/programmer places prefetch instructions
Put prefetched value into…
  Register (binding, also called “hoisting”)
    May prevent instructions from committing
  Cache (non-binding)
    Requires ISA support
    May get evicted from cache before demand

## Slide 7: Software Prefetching (2/4)
A
C
B
R3 = R1+4
R1 = [R2]
A
C
B
R1 = [R2]
R3 = R1+4
(Cache misses in red)
Hopefully the load miss
is serviced by the time
we get to the consumer
R1 = R1- 1
R1 = R1- 1
Hoisting must
be aware of
dependencies
A
C
B
R1 = [R2]
R3 = R1+4
PREFETCH[R2]
Using a prefetch instruction
can avoid problems with
data dependencies

## Slide 8: Software Prefetching (3/4)
  for (I = 1; I < rows; I++)
  {
  for (J = 1; J < columns; J++)
  {
  prefetch(&x[I+1,J]);
  sum = sum + x[I,J];
  }
  }

## Slide 9: Software Prefetching (4/4)
Pros:
  Gives programmer control and flexibility
  Allows time for complex (compiler) analysis
  No (major) hardware modifications needed
Cons:
  Hard to perform timely prefetches
    At IPC=2 and 100-cycle memory  move load 200 inst. earlier
    Might not even have 200 inst. in current function
  Prefetching earlier and more often leads to low accuracy
    Program may go down a different path
  Prefetch instructions increase code footprint
    May cause more I$ misses, code alignment issues
Notes: hoisting of regular loads needs to be safe, too (if moved to an earlier block, is the load’s address still valid or can the load now cause a fault?). Prefetch instructions usually able to “fail” silently without any side-effects.

## Slide 10: Hardware Prefetching (1/3)
Hardware monitors memory accesses
  Looks for common patterns
Guessed addresses are placed into prefetch queue
  Queue is checked when no demand accesses waiting
Prefetchers look like READ requests to the hierarchy
  Although may get special “prefetched” flag in the state bits
Prefetchers trade bandwidth for latency
  Extra bandwidth used only when guessing incorrectly
  Latency reduced only when guessing correctly
  No need to change software

## Slide 11: Hardware Prefetching (2/3)
Processor
Registers
L1 I-Cache
L1 D-Cache
L2 Cache
D-TLB
I-TLB
Main Memory (DRAM)
L3 Cache (LLC)
Potential
Prefetcher
Locations

## Slide 12: Hardware Prefetching (3/3)
Processor
Real CPUs have multiple prefetchers
  Usually closer to the core (easier to detect patterns)
  Prefetching at LLC is hard (cache is banked and hashed)
Registers
L1 I-Cache
L1 D-Cache
L2 Cache
D-TLB
I-TLB
L3 Cache (LLC)
Intel Core2
Prefetcher
Locations

## Slide 13: Next-Line (or Adjacent-Line) Prefetching
On request for line X, prefetch X+1 (or X^0x1)
  Assumes spatial locality
    Often a good assumption
  Should stop at physical (OS) page boundaries
Can often be done efficiently
  Adjacent-line is convenient when next-level block is bigger
  Prefetch from DRAM can use bursts and row-buffer hits
Works for I$ and D$
  Instructions execute sequentially
  Large data structures often span multiple blocks
  Simple, but usually not timely
Notes: crossing page boundaries can cause issues. First, the page may not be mapped and you probably don’t want to take a page fault due to a prefetch that you don’t even know for sure whether it’ll be useful or not. Second, the next physically contiguous page may not have anything to do with where the next virtual page is physically located.

## Slide 14: Next-N-Line Prefetching
On request for line X, prefetch X+1, X+2, …, X+N
  N is called “prefetch depth” or “prefetch degree”
Must carefully tune depth N. Large N is …
  More likely to be useful (correct and timely)
  More aggressive  more likely to make a mistake
    Might evict something useful
  More expensive  need storage for prefetched lines
    Might delay useful request on interconnect or port
  Still simple, but more timely than Next-Line

## Slide 15: Stream Buffers (1/3)
What if we have multiple inter-twined streams?
  A, B, A+1, B+1, A+2, B+2, …
Can use multiple stream buffers to track streams
  Keep next-N available in buffer
  On request for line X, shift buffer and fetch X+N+1 into it
Can extend to “quasi-sequential” stream buffer
  On request Y in [X…X+N], advance by Y-X+1
  Allows buffer to work when items are skipped
  Requires expensive (associative) comparison

## Slide 16: Stream Buffers (2/3)
Figures from Jouppi “Improving Direct-Mapped Cache Performance by the
Addition of a Small Fully-Associative Cache and Prefetch Buffers,” ISCA’90

## Slide 17: Stream Buffers (3/3)
  Can support multiple streams in parallel

## Slide 18: Stride Prefetching (1/2)
Access patterns often follow a stride
  Accessing column of elements in a matrix
  Accessing elements in array of structs
Detect stride S, prefetch depth N
  Prefetch X+1∙S, X+2∙S, …, X+N∙S
Column in matrix
Elements in array of structs

## Slide 19: Stride Prefetching (2/2)
Must carefully select depth N
  Same constraints as Next-N-Line prefetcher
How to determine if A[i]  A[i+1] or X  Y ?
  Wait until A[i+2] (or more)
  Can vary prefetch depth based on confidence
    More consecutive strided accesses  higher confidence
New access to
A+3N
Stride
Count
A+2N
N
2
+
A+4N
+
=
Update count
>2
Do prefetch?
Last Addr

## Slide 20: “Localized” Stride Prefetchers (1/2)
What if multiple strides are interleaved?
  No clearly-discernible stride
  Could do multiple strides like stream buffers
    Expensive (must detect/compare many strides on each access)
  Accesses to structures usually localized to an instruction
Miss pattern looks like:
A, X, Y, A+N, X+N, Y+N, A+2N, X+2N, Y+2N, …
(X-A)
(Y-X)
(A+N-Y)
  Use an array of strides, indexed by PC
(X-A)
(Y-X)
(A+N-Y)
(X-A)
(Y-X)
(A+N-Y)
Load R1 = [R2]
Load R3 = [R4]
Store [R6] = R5
Add R5, R1, R3

## Slide 21: “Localized” Stride Prefetchers (2/2)
Store PC, last address, last stride, and count in RPT
On access, check RPT (Reference Prediction Table)
  Same stride?  count++ if yes, count-- or count=0 if no
  If count is high, prefetch (last address + stride*N)
PCa: 0x409A34
Load R1 = [R2]
PCb: 0x409A38
Load R3 = [R4]
PCc: 0x409A40
Store [R6] = R5
0x409
Tag
Last Addr
Stride
Count
0x409
0x409
A+3N
N
2
X+3N
N
2
Y+2N
N
1
If confident
about the stride
(count > Cmin),
prefetch
(A+4N)
+

## Slide 22: Other Patterns
Sometimes accesses are regular, but no strides
  Linked data structures (e.g., lists or trees)
A
B
C
D
E
F
Linked-list traversal
F
A
B
C
D
E
Actual memory
layout
(no chance to detect a stride)

## Slide 23: Pointer Prefetching (1/2)
Data filled on cache miss
(512 bits of data)
1
4128
90120230
90120758
8029
0
14
4128
Nope
Nope
Maybe!
Maybe!
struct bintree_node_t {
int data1;
int data2;
struct bintree_node_t * left;
struct bintree_node_t * right;
};
This allows you to walk the tree
(or other pointer-based data structures
which are typically hard to prefetch)
  Pointers usually “look different”
Go ahead and prefetch these
(needs some help from the TLB)
Nope
Nope
Nope
Nope
90120230
90120758
Notes: needs extra help from TLB… addresses are virtual, but L2 cache is typically physically-addressed/physically-tagged.

## Slide 24: Pointer Prefetching (2/2)
Relatively cheap to implement
  Don’t need extra hardware to store patterns
Limited lookahead makes timely prefetches hard
  Can’t get next pointer until fetched data block
X
Access Latency
Access Latency
Access Latency
Stride Prefetcher:
A
Access Latency
B
Access Latency
C
Access Latency
Pointer Prefetcher:
X+N
X+2N

## Slide 25: Pair-wise Temporal Correlation (1/2)
Accesses exhibit temporal correlation
  If E followed D in the past  if we see D, prefetch E
Correlation Table
D
F
A
B
C
E
E
?
B
C
D
F
A
B
C
D
E
F
Linked-list traversal
F
A
B
C
D
E
Actual memory layout
10
00
11
11
11
01
D
F
A
B
C
E
  Can use recursively to get more lookahead 

## Slide 26: Pair-wise Temporal Correlation (2/2)
Many patterns more complex than linked lists
  Can be represented by a Markov Model
  Required tracking multiple potential successors
Number of candidates is called breadth
A
B
C
D
E
F
1.0
.33
.5
.2
1.0
.6
.2
.67
.6
.5
.2
.2
Correlation Table
D
F
A
B
C
E
C
E
B
C
D
A
11
11
11
11
11
11
E
?
C
?
F
?
01
00
01
00
10
00
D
F
A
B
C
E
  Recursive breadth & depth grows exponentially 
Markov Model

## Slide 27: Increasing Correlation History Length
Longer history enables more complex patterns
  Use history hash for lookup
  Increases training time
A
B
C
D
E
F
G
DFS traversal: ABDBEBACFCGCA
A
B
B
D
D
B
B
E
E
B
B
A
A
C
D
B
E
B
A
C
F
  Much better accuracy , exponential storage cost 

## Slide 28: Spatial Correlation (1/2)
Irregular layout  non-strided
Sparse  can’t capture with cache blocks
But, repetitive  predict to improve MLP
Database Page in Memory (8kB)
page header
tuple data
tuple slot index
Memory
  Large-scale repetitive spatial access patterns

## Slide 29: Spatial Correlation (2/2)
Logically divide memory into regions
Identify region by base address
Store spatial pattern (bit vector) in correlation table
Region A
Region B
Correlation Table
PCx: A’
PCy: B’
110…1010001…111
110…0001101…111
PCx
PCy
+
To prefetch Queue

## Slide 30: Evaluating Prefetchers
Compare against larger caches
  Complex prefetcher vs. simple prefetcher with larger cache
Primary metrics
  Coverage: prefetched hits / base misses
  Accuracy: prefetched hits / total prefetches
  Timeliness: latency of prefetched blocks / hit latency
Secondary metrics
  Pollution: misses / (prefetched hits + base misses)
  Bandwidth: total prefetches + misses / base misses
  Power, Energy, Area...

## Slide 31: Hardware Prefetcher Design Space
What to prefetch?
  Predictors regular patterns (x, x+8, x+16, …)
  Predicted correlated patterns (A…B->C, B..C->J, A..C->K, …)
When to prefetch?
  On every reference  lots of lookup/prefetcher overhead
  On every miss  patterns filtered by caches
  On prefetched-data hits (positive feedback)
Where to put prefetched data?
  Prefetch buffers
  Caches

## Slide 32: What’s Inside Today’s Chips
Data L1
  PC-localized stride predictors
  Short-stride predictors within block  prefetch next block
Instruction L1
  Predict future PC  prefetch
L2
  Stream buffers
  Adjacent-line prefetch