## Slide 1: COMP 590-154: Computer Architecture
Out-of-Order Memory Access

## Slide 2: Dynamic Scheduling Summary
Out-of-order execution: a performance technique
Feature I: Dynamic scheduling (iO  OoO)
  “Performance” piece: re-arrange insns. for high perf.
  Decode (iO)  dispatch (iO) + issue (OoO)
  Two algorithms: Scoreboard, Tomasulo
Feature II: Precise state (OoO  iO)
  “Correctness” piece: put insns. back into program order
  Writeback (OoO)  complete (OoO) + retire (iO)
  Two designs: P6, R10K
  One remaining piece: OoO memory accesses

## Slide 3: Executing Memory Instructions
If R1 != R7
  Then Load R8 gets correct value from cache
If R1 == R7
  Then Load R8 should get value from the Store
  But it didn’t!
Load R3 = 0[R6]
Add R7 = R3 + R9
Store R4  0[R7]
Sub R1 = R1 – R2
Load R8 = 0[R1]
Issue
Issue
Cache Miss!
Issue
Cache Hit!
Miss serviced…
Issue
Issue
But there was a later load…
Notes: Basic example of address-based dependency ambiguities

## Slide 4: Memory Disambiguation Problem
Ordering problem is a data-dependence violation
Imprecise memory worse than imprecise registers
Why can’t this happen with non-memory insts?
  Operand specifiers in non-memory insns. are absolute
    “R1” refers to one specific location
  Operand specifiers in memory insns. are ambiguous
    “R1” refers to a memory location specified by the value of R1.
    When pointers (e.g., R1) change, so does this location

## Slide 5: Two Problems
Memory disambiguation on loads
  Do earlier unexecuted stores to the same address exist?
    Binary question: answer is yes or no
Store-to-load forwarding problem
  I’m a load: Which earlier store do I get my value from?
  I’m a store: Which later load(s) do I forward my value to?
    Non-binary question: answer is one or more insn. identifiers

## Slide 6: Load/Store Queue (1/3)
Load/store queue (LSQ)
  Completed stores write to LSQ
  When store retires, head of LSQ written to L1-D
  When loads execute, access LSQ and L1-D in parallel
    Forward from LSQ if older store with matching address

## Slide 7: Load/Store Queue (2/3)
regfile
L1-D
I$
B
P
ROB
LSQ
load/store
store data
addr
load data
  Almost a “real” processor diagram

## Slide 8: Load/Store Queue (3/3)
L
0xF048
41773
0x3290
42
L/S
PC
Seq
Addr
Value
S
0xF04C
41774
0x3410
25
S
0xF054
41775
0x3290
-17
L
0xF060
41776
0x3418
1234
L
0xF840
41777
0x3290
-17
L
0xF858
41778
0x3300
1
S
0xF85C
41779
0x3290
0
L
0xF870
41780
0x3410
25
L
0xF628
41781
0x3290
0
L
0xF63C
41782
0x3300
1
Oldest
Youngest
0x3290
42
0x3410
38
0x3418
1234
0x3300
1
Data Cache
25
-17

## Slide 9: In-order Memory (Policy 1/4)
No memory reordering
LSQ still needed for forwarded data (last slide)
Easy to schedule
Ready!
bid
grant
bid
grant
Ready!
1 (“head” pointer)
…
…
  Fairly simple, but low performance

## Slide 10: Loads OoO between Stores (Policy 2/4)
Loads exec OoO w.r.t. each other
  Stores block everything
S
ready
issued
L
L
S
L
S=0
L=1
1 (“head” pointer)
  Still simple, but better performance

## Slide 11: Stores Can be Split into STA/STD
STA: STore Address
STD: STore Data
Makes some designs easier
  RS/ROB store one value
  Stores need two (A & D)
Store
dispatch/
alloc
STA
STD
LD
“store”
“load”
LSQ
RS
schedule
Add
Load

## Slide 12: Loads Wait for STAs Only (Policy 3/4)
Only address is needed to disambiguate
May be ready earlier to allow checking for violations
  No need to wait for data
S
L
Address ready
Data ready
  Still simple, even better performance

## Slide 13: Loads Execute When Ready (Policy 4/4)
Most aggressive approach
Relies on fact that storeload forwarding is rare
Greatest potential IPC – loads never stall
Potential for incorrect execution
  Need to be able to “undo” bad loads
  Very complex, but high performance
Notes: Perhaps good to have discussion here about when forwarding is unlikely vs. likely. ISA dependence? Program structures?

## Slide 14: Detecting Ordering Violations (1/2)
Case 1: Older store execs before younger load
  No problem; if same address stld forwarding happens
Case 2: Older store execs after younger load
  Store scans all younger loads
  Address match  ordering violation

## Slide 15: Detecting Ordering Violations (2/2)
L
0xF048
41773
0x3290
42
S
0xF04C
41774
0x3410
25
S
0xF054
41775
0x3290
-17
L
0xF060
41776
0x3418
1234
L
0xF840
41777
0x3290
-17
L
0xF858
41778
0x3300
1
S
0xF85C
41779
0x3290
0
L
0xF870
41780
0x3410
25
L
0xF628
41781
0x3290
42
L
0xF63C
41782
0x3300
1
Store broadcasts value,
address and sequence #
(-17,0x3290,41775)
Loads CAM-match on
address, only care if
store seq-# is lower than
own seq
(Load 41773 ignores broadcast because it has a lower seq #)
IF younger load hadn’t executed, and
address matches, grab broadcasted value
IF younger load has executed, and
address matches, then ordering violation!
-17
(0,0x3290,41779)
An instruction may be involved in
more than one ordering violation
L/S
PC
Seq
Addr
Value
  Must flush all later accesses after violation
Notes: Note that detecting address matches is actually not as trivial as you might think. Consider x86 where loads/stores may be multiple bytes wide and unaligned. A store may write to one or more bytes, of which only a subset overlap with some of the bytes read by a load. The overlap must be detected to ensure correct execution, although forwarding may be restricted to certain “easy” cases (e.g., perfect alignment)… for the unsupported forwarding cases, you can always stall the load until the matching store or stores writeback to the cache and the load can read its value out directly from the cache. It seems that each generation of Intel Core processors is gradually supporting more forwarding cases.

## Slide 16: Dealing with Misspeculations
Loads are not the only thing which are wrong
  Loads propagate wrong values to all dependents
These must somehow be re-executed
Easiest: flush all instructions after (and including?) the misspeculated load, and just refetch
Load uses forwarded value
Correct value propagated when instructions re-execute
Notes: For x86, you probably want to flush *including* the load because the load may be part of a longer uop-flow, and so refetching just part of a flow does not make any sense (i.e., how do you resteer the front-end in this case?). Consider the CALL(with memory argument) instruction which decomposes, among other uops, into a load (which reads in the new PC) and a jump (to the new PC). The jump portion may have already jumped to the wrong place, but there is no easy way to redo only those uops in the flow following the load.

## Slide 17: Flushing Complications
Exactly same mispredicted branches
  Checkpoint at every load in addition to branches
    Very large number of checkpoints needed
  Rollback to previous branch (which has its own checkpoint)
    Make sure load doesn’t misspeculate on 2nd try
    Must redo work between the branch and the load
  Can work with undo-list style of recovery
Not all younger insns. are dependent on bad load
Pipeline latency due to refetch is exposed

## Slide 18: Selective Re-Execution
Re-execute only the dependent insns.
Ideal case w.r.t. maintaining high IPC
  No need to re-fetch/re-dispatch/re-rename/re-execute
Very complicated
  Need to hunt down only data-dependent insns.
  Some bad insns. already executed (now in ROB)
  Some bad insns. didn’t execute yet (still in RS)
P4 does something like this (called “replay”)
Notes: Well, you could perhaps force replay to work, but you’d basically have to have a giant replay queue to hold all instructions until you can guarantee that they will not be down-stream from a load-store ordering violation.

## Slide 19: LSQ Hardware in More Detail
Very complicated CAM logic
  Need to quickly look up based on value
  May find multiple values / need age based search
No need for age-based search in ROB
  Physical regs. are renamed, guarantees one writer
  No easy way to prevent multiple stores to same address

## Slide 20: Loads Checking for Earlier Stores
On Load dispatch, find data from earlier Store
ST 0x4000
ST 0x4000
ST 0x4120
LD 0x4000
=
Address Bank
Data Bank
=
=
=
=
=
=
0
No earlier
matches
Addr match
Valid store
Use this
store
Need to adjust this so that
load need not be at bottom,
and LSQ can wrap-around
If |LSQ| is large, logic can be
adapted to have log delay
Notes: As mentioned in the earlier notes, the real circuitry gets quite a bit messier when you have to deal with different memory widths and/or unaligned accesses.

## Slide 21: Data Forwarding
Similar Logic to Previous Slide
On execute Store (STA+STD), check for later Loads
ST 0x4000
ST 0x4120
LD 0x4000
Addr Match
Is Load
Capture
Value
Overwritten
Overwritten
Data Bank
  This is ugly, complicated, slow, and power hungry
ST 0x4000
Notes: This logic must handle the situation where more than one store writes to the same address. The load should only pick up a value from the most recent matching store… which may hard to tell if some store addresses have not yet been computed.

## Slide 22: Alternative Data Forwarding: Store Colors
Each store assigned unique number (its color)
Loads inherit the color of the most recent store
St
St
St
St
Ld
Ld
Ld
Ld
Color=1
Color=2
Color=3
Color=4
Ld
All three loads have same color:
only care about ordering w.r.t.
stores, not other loads
St
Ld
Ld
Ld
Ignore store broadcasts
If store’s color > your own

## Slide 23: Split Load Queue/Store Queue
Stores don’t need to broadcast address to stores
Loads don’t need to check against earlier loads
Store Queue (STQ)
Load Queue (LDQ)
Associative search for earlier stores only needs
to check entries that actually contain stores
Associative search
for later loads for
STLD forwarding
only needs to check
entries that actually
contain loads
Notes: Pretty much all modern out-of-order processors use split LDQ/STQs. The latency of the broadcast/CAMs on each queue will be faster since each queue is smaller than what you would have if you combined them all into one giant unified queue.